## Slide 1: Systematic Evaluation of Signal-to-Image Transformation Pipelines for Vision Transformer-based Sleep Stage Classification
BioMed Frontiers 2026
International Conference on Biomedical Innovation
Janith R.R.H. Ramanayakage and Chandima N.P.G. Arachchige
Department of Statistics, Faculty of Science, University of Colombo, Sri Lanka
Paper ID: 45

## Slide 2: Why automate sleep staging?
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
Sleep disorders (insomnia, apnoea, narcolepsy) are widespread
Gold standard: manual scoring of polysomnography (PSG)
Slow and subjective: hours per night; experts disagree
Deep learning: CNN/RNN → Vision Transformers (ViTs)
1–3 h
to score one full-night recording
82.6%
inter-scorer agreement, experienced experts
50–70 M
US adults living with a sleep disorder
Two scoring standards
R&K: Wake, S1, S2, S3, S4, REM (used here)
AASM: W, N1, N2, N3, R (S3 + S4 merged)

## Slide 3: Research gap and objectives
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
The gap
Prior ViT work uses spectrograms or raw signals only
GASF, GADF and MTF never compared for ViTs
Best sampling rate before imaging unknown
Pre-training value on PSG images unclear
Four experiments
1
Image transformation: GASF, GADF, MTF, spectrogram
2
Sampling rate: 512 / 256 / 128 / 64 Hz, FFT vs DWT
3
Pre-trained vs from-scratch ViT, balanced vs imbalanced
4
Seven architectures incl. ResNet-50 baseline

## Slide 4: Dataset: CAP Sleep Database
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
80
recordings (6 healthy, 74 patients)
80,667
30-second epochs
16
channels at 512 Hz
6
stages: Wake, S1–S4, REM
Subject-wise 5-fold CV: no subject in both train and test
Chart: Epoch share by sleep stage
| Wake | S1 | S2 | S3 | S4 | REM
Epochs (%) | 13.5 | 6.5 | 47.7 | 10.5 | 8.6 | 13.3

## Slide 5: Proposed Pipeline
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
Figure 1. Overall five-stage pipeline

## Slide 6: Four Signal-to-Image transformations
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
GASF
Gramian Angular Summation Field
Summed angles; preserves global temporal correlation
GADF
Gramian Angular Difference Field
Difference of angles; less globally coherent
MTF
Markov Transition Field
32 bins; quantisation loss, slow (5 s/epoch)
Spectrogram
STFT, Hamming 256
Fixed time–frequency resolution
16 images → 4×4 grid → 224×224×3 → ViT-B/16

## Slide 7: Same epoch, four images
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
One subject, one 30 s epoch, original 512 Hz: 16 channels tiled into a 4×4 composite
Angle difference
Angle sum
Time–frequency (STFT)
Transition probabilities
The encoding changes the texture the ViT sees; GASF keeps rich structure

## Slide 8: GASF performs best
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
EXPERIMENT
Chart: 
| GASF | GADF | MTF | Spectrogram
Accuracy (%) | 78.5 | 77.2 | 75.8 | 74.1
78.5%
GASF accuracy (macro-F1 0.773)
5.0 s
MTF time per epoch vs 0.2 s for GASF
GASF ≈ GADF; both clearly beat MTF and spectrogram

## Slide 9: Downsampling: FFT vs DWT
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
FFT
DWT
What to look for
GASF images of the same epoch, resampled to 64, 128, 256 Hz and the 512 Hz original.
FFT: image structure stays almost the same at every rate.
DWT: images change visibly below 256 Hz; 128 Hz is the sweet spot for accuracy (next slide).
Same epoch, same GASF encoding; only the resampling method differs

## Slide 10: DWT at 128 Hz is optimal
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
EXPERIMENT
Chart: 
| 64 Hz | 128 Hz | 256 Hz | 512 Hz
DWT | 75.9 | 80.3 | 79.1 | 78.5
FFT | 73.5 | 76.2 | 77.8 | 78.5
80.3%
DWT @ 128 Hz (macro-F1 0.791)
+1.8 pp
over original 512 Hz signals
DWT beats FFT at every reduced rate; peak at 128 Hz

## Slide 11: Class balancing with DCGAN
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
Real GASF composite vs DCGAN-generated sample, same class
How it works
A DCGAN learns the GASF composites of each under-represented class.
Synthetic images are added to training folds only.
Test folds stay 100% real, so there is no leakage.
Synthetic samples keep the 4×4 channel layout and balance the classes

## Slide 12: Pre-training adds 11+ points
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
EXPERIMENT
Chart: 
| Balanced | Imbalanced
Pre-trained ViT-B/16 | 86.2 | 80.5
From scratch | 74.8 | 68.3
+11.4 pp
balanced: 86.2% vs 74.8%
+12.2 pp
imbalanced: 80.5% vs 68.3%
Balancing (DCGAN, training folds only) adds ≈ 5.7 pp

## Slide 13: ViT-B/16 beats other models
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
EXPERIMENT
Chart: 
| ResNet-50 | PVT-Small | ViT-B/32 | DeiT-B | BEiT-B | Swin-B | ViT-B/16
Accuracy (%) | 76.2 | 81.8 | 83.2 | 84.3 | 84.6 | 85.1 | 86.2
86.2%
ViT-B/16 (macro-F1 0.853)
+10.0 pp
over ResNet-50 CNN baseline
Transformers outperform the CNN; PVT-Small is the efficient option

## Slide 14: Class-wise results and limitations
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
Chart: Per-class F1 score
| Wake | S1 | S2 | S3 | S4 | REM
Balanced | 0.905 | 0.721 | 0.922 | 0.8 | 0.784 | 0.795
Imbalanced | 0.852 | 0.512 | 0.887 | 0.667 | 0.647 | 0.851
Limitations
S1 (6.5% of data) is weakest
Single database; no cross-dataset test
R&K labels, not AASM
No formal significance tests
4×4 channel layout not ablated

## Slide 15: Conclusions and future work
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
Best pipeline
GASF image encoding
DWT resampling to 128 Hz
Fine-tuned ImageNet ViT-B/16
86.2% accuracy, 0.853 macro-F1
Future work
Multimodal fusion
Lightweight ViTs for edge use
Cross-dataset validation

## Slide 16: Thank you
BioMed Frontiers 2026
International Conference on Biomedical Innovation
Questions?
janithramanayake523@gmail.com
Paper ID: 45
Code on GitHub