## Slide 1: Systematic Evaluation of Signal-to-Image Transformation Pipelines for Vision Transformer-based Sleep Stage Classification
BioMed Frontiers 2026
International Conference on Biomedical Innovation
Janith R.R.H. Ramanayakage and Chandima N.P.G. Arachchige
Department of Statistics, Faculty of Science, University of Colombo, Sri Lanka
Paper ID: 45

## Slide 2: Why automate sleep staging?
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
Sleep disorders (insomnia, apnoea, narcolepsy) are widespread
Gold standard: manual scoring of polysomnography (PSG)
Slow and subjective: hours per night; experts disagree
Deep learning: CNN/RNN → Vision Transformers (ViTs)
2–4 h
to score one full-night recording
82.6%
inter-scorer agreement, experienced experts
50–70 M
US adults living with a sleep disorder

## Slide 3: Research gap and objectives
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
The gap
Prior ViT work uses spectrograms or raw signals only
GASF, GADF and MTF never compared for ViTs
Best sampling rate before imaging unknown
Pre-training value on PSG images unclear
Four experiments
1
Image transformation: GASF, GADF, MTF, spectrogram
2
Sampling rate: 512 / 256 / 128 / 64 Hz, FFT vs DWT
3
Pre-trained vs from-scratch ViT, balanced vs imbalanced
4
Seven architectures incl. ResNet-50 baseline

## Slide 4: Dataset: CAP Sleep Database
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
80
recordings (6 healthy, 74 patients)
80,667
30-second epochs
16
channels at 512 Hz
6
stages: Wake, S1–S4, REM
Subject-wise 5-fold CV: no subject in both train and test
Chart: Epoch share by sleep stage
| Wake | S1 | S2 | S3 | S4 | REM
Epochs (%) | 13.5 | 6.5 | 47.7 | 10.5 | 8.6 | 13.3

## Slide 5: Proposed pipeline
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
Figure 1. Overall five-stage pipeline

## Slide 6: Four signal-to-image transformations
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
GASF
cos(φᵢ + φⱼ)
Summed angles; preserves global temporal correlation
GADF
sin(φᵢ − φⱼ)
Difference of angles; less globally coherent
MTF
Markov transition probs
32 bins; quantisation loss, slow (5 s/epoch)
Spectrogram
STFT, Hamming 256
Fixed time–frequency resolution
16 images → 4×4 grid → 224×224×3 → ViT-B/16

## Slide 7: GASF performs best
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
EXPERIMENT
Chart: 
| GASF | GADF | MTF | Spectrogram
Accuracy (%) | 78.5 | 77.2 | 75.8 | 74.1
78.5%
GASF accuracy (macro-F1 0.773)
5.0 s
MTF time per epoch vs 0.2 s for GASF
GASF ≈ GADF; both clearly beat MTF and spectrogram

## Slide 8: DWT at 128 Hz is optimal
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
EXPERIMENT
Chart: 
| 64 Hz | 128 Hz | 256 Hz | 512 Hz
DWT | 75.9 | 80.3 | 79.1 | 78.5
FFT | 73.5 | 76.2 | 77.8 | 78.5
80.3%
DWT @ 128 Hz (macro-F1 0.791)
+1.8 pp
over original 512 Hz signals
DWT beats FFT at every reduced rate; peak at 128 Hz

## Slide 9: Pre-training adds 11+ points
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
EXPERIMENT
Chart: 
| Balanced | Imbalanced
Pre-trained ViT-B/16 | 86.2 | 80.5
From scratch | 74.8 | 68.3
+11.4 pp
balanced: 86.2% vs 74.8%
+12.2 pp
imbalanced: 80.5% vs 68.3%
Balancing (DCGAN, training folds only) adds ≈ 5.7 pp

## Slide 10: ViT-B/16 beats other models
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
EXPERIMENT
Chart: 
| ResNet-50 | PVT-Small | ViT-B/32 | DeiT-B | BEiT-B | Swin-B | ViT-B/16
Accuracy (%) | 76.2 | 81.8 | 83.2 | 84.3 | 84.6 | 85.1 | 86.2
86.2%
ViT-B/16 (macro-F1 0.853)
+10.0 pp
over ResNet-50 CNN baseline
Transformers outperform the CNN; PVT-Small is the efficient option

## Slide 11: Class-wise results and limitations
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
Chart: Per-class F1 score
| Wake | S1 | S2 | S3 | S4 | REM
Balanced | 0.905 | 0.721 | 0.922 | 0.8 | 0.784 | 0.795
Imbalanced | 0.852 | 0.512 | 0.887 | 0.667 | 0.647 | 0.851
Limitations
S1 (6.5% of data) is weakest
Single database; no cross-dataset test
R&K labels, not AASM
No formal significance tests
4×4 channel layout not ablated

## Slide 12: Conclusions and future work
BioMed Frontiers 2026 | International Conference on Biomedical Innovation
Best pipeline
GASF image encoding
DWT resampling to 128 Hz
Fine-tuned ImageNet ViT-B/16
86.2% accuracy, 0.853 macro-F1
Future work
Multimodal fusion
Lightweight ViTs for edge use
Cross-dataset validation

## Slide 13: Thank you
BioMed Frontiers 2026
International Conference on Biomedical Innovation
Questions?
janithramanayake523@gmail.com
Paper ID: 45